6380013 (Gold Tone w/Brown Leather Band) Talking Dress Calendar Watch  Instructions

Features include:

• Quick alarm on/off feature

• “3 second hold” setting to prevent changing settings inadvertently

Functions in Normal Time Mode:

Press “S1” to activate voice saying time.

Press “S3” to activate voice saying day, date and year

Press “S4” to turn alarm on or off

Press “S3” to hear alarm status and alarm time (if on)

Setting Instructions for Analog Time:

Gently pull crown out until you feel a click.

Turn crown to set hour and minute hands.

Push crown back in to set time.

Setting Instructions for Talking Time, Date, Alarm and Chime:

To activate setting mode, press and hold “S4” for 3 seconds. Once you hear “chime on” you will know you are in setting mode.

Press button “S4” to navigate through the different functions to set. Once you reach the desired function, then use button “S2” to adjust.

For example, to set the time, press “S4” until you hear

”Time Hour Setting”, then press”S2” to move to the desired hour. Press “S4” again to hear “Time Minute Setting”, then press “S2” to move to the desired minute. This same process is used to set chime, alarm, date and time functions.